Permit No. VA0089729

Page 1 of 11

PART I

A. 	EFFLUENT LIMITATIONS AND MONITORING REQUIREMENTS

1.	During the period beginning with the permit's effective date and lasting until the permit's expiration date, the permittee is authorized to discharge from outfall serial number 001.

Such discharges shall be limited and monitored by the permittee as specified below:

| EFFLUENT CHARACTERISTICS |  |  |  |  | DISCHARGE LIMITATIONS |  |  |  | MONITORING REQUIREMENTS |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | Monthly Average |  | Weekly Average |  | Minimum | Maximum | Frequency | Sample Type |
| Flow (MGD)2 |  |  | NL |  | NA |  | NA | NL | Continuous | T/I/R |
| pH (standard units) |  |  | NA |  | NA |  | 6.0 | 9.0 | 1/Day | Grab |
| CBOD5 (June-November) |  |  | 7.3 mg/l | 6.1 kg/d | 10.9 mg/l | 9.1 kg/d | NA | NA | 3 Days/Week | 8 HC |
| CBOD5 (December-May) |  |  | 25 mg/l | 20.8 kg/d | 37.5 mg/l | 31.2 kg/d | NA | NA | 3 Days/Week | 8 HC |
| TKN (June-November) |  |  | 3.0 mgl | 2.5 kg/d | 4.5 mg/l | 3.7 kg/d | NA | NA | 3 Days/Week | 8 HC |
| Suspended Solids |  |  | 30 mg/l | 25 kg/d | 45 mg/l | 37 kg/d | NA | NA | 3 Days/Week | 8 HC |
| Total Residual Chlorine (TRC) (mg/l)3 |  |  | NA |  | NA |  | NA | NA | 3/Day @ 4-Hr. Intervals | Grab |
| Dissolved Oxygen (mg/l) |  |  | NA |  | NA |  | 7.0 | NA | 1/Day | Grab |
| Ammonia-N (December-May)4 |  |  | 4.0 mg/l | 3.33 kg/d | 4.0 mg/l | 3.33 kg/d | NA | NA | 1/Month | 8 HC |
| Ammonia-N (June-November)4 |  |  | 1.0 mg/l | 0.83 kg/d | 1.0 mg/l | 0.83 kg/d | NA | NA | 1/Month | 8 HC |

T/I/R = Totalizing, Indicating and Recording Equipment

NL = No Limitation, monitoring required

NA = Not Applicable

2.	The design flow of this treatment facility is 0.22 MGD.

3.	See Part I.B. for TRC limitations.

4.	See Part I.C. for additional monitoring instructions.

5.	There shall be no discharge of floating solids or visible foam in other than trace amounts.